Software board general agreement

I. Overview

This protocol is a universal protocol for the RS485/RS232/UART interface of the Polar Air Active Balance Protection Board, and the baud rate is 9600bps.

II. The frame structure

In the communication process, the protection board is always the slave and the remote device is the master. All communication can only be initiated by the master and responded by the slave. To facilitate the distinction, it is agreed that the frame sent by the host is the configuration frame, and the frame sent by the protection board is the response frame.
The configuration frame includes start bit, status bit, command code, data length, data content, checksum, and stop bit. The frame structure is as follows:

| Start bit | Status bit | Command code | Data length | Data content | check | Stop bit |
| --- | --- | --- | --- | --- | --- | --- |

among them:

- Start bit: 1 byte, indicating the start of a frame of data, fixed to 0xDD;

- Status bit: 1 byte, status 0xA5 means read, status 0x5A means write.

- Command code: 1 byte. In the communication process, the command code is used to distinguish the data content carried in the configuration frame. The corresponding relationship between each command code and the data carried is as follows:

| Status bit | Command code | Data content |
| --- | --- | --- |
| 0xA5 | 0x03 | Read basic information and status |
|  | 0x04 | Read battery cell voltage |
|  | 0x05 | Read the hardware version number of the protection board |
|  | 0x06 | Read the private data of the protection board user |
| 0x5A | 0xE1 | MOS control instructions |

- Data length: 1 byte, indicating the effective length of the data carried in the frame.

- Data content: N bytes, the content carried by the frame data, when the data length is 0, there is no such part.

- Verification: 2 bytes, the verification field is "command code + length byte + data segment content", the verification method is the sum of the above fields and then the inverse plus 1, the high bit is in the front and the low bit is in the back.

- Stop bit: 1 byte, indicating the end of a frame of data, fixed as 0x77;

The response frame contains the start bit, status bit, command code, data length, data content, checksum, and stop bit. The frame structure is as follows:

| Start bit | Command code | Status bit | Data length | Data content | check | Stop bit |
| --- | --- | --- | --- | --- | --- | --- |

among them:

- Start bit: 1 byte, indicating the start of a frame of data, fixed to 0xDD;

- Command code: 1 byte, which is the command code of the configuration frame that this frame responds to.

- Status bit: 1 byte, 0x00 means correct, 0x80 means error.

- Data length: 1 byte, indicating the effective length of the data carried in the frame.

- Data content: N bytes, the content carried by the frame data, when the data length is 0, there is no such part.

- Verification: 2 bytes, the verification field is "command code + length byte + data segment content", the verification method is the sum of the above fields and then the inverse plus 1, the high bit is in the front and the low bit is in the back.

- Stop bit: 1 byte, indicating the end of a frame of data, fixed as 0x77;

III. Communication example

- Read basic information and status

Host computer send: DD A5 03 00 FF FD 77

BMS response: DD 03 00 1B 17 00 00 00 02 D0 03 E8 00 00 20 78 00 00 00 00 00 00 10 48 03 0F 02 0B 76 0B 82 FB FF 77

Red is the checked byte, which is the sum of all bytes; the latter 2 are the check results, which are the sum of all the check data in the front and then take the inverse +1.
The data content structure of the response frame is as follows:

| Data content | length | Description |
| --- | --- | --- |
| Total voltage | 2 Byte | Unit: 10mV; high byte first, low byte last. |
| Total current | 2 Byte | Unit: 10mA; judge the battery charge and discharge status by current, charge is positive, discharge is negative |
| The remaining capacity | 2 Byte | Unit: 10mAh; |
| Nominal capacity | 2 Byte | Unit: 10mAh; |
| Cycles | 2 Byte | Unit: times; |
| Production Date | 2 Byte | Use 2 bytes to transmit such as 0x2068, where the date is the lowest 5: 0x2028&0x1F = 8 means the date; month (0x2068>>5)&0x0f = 0x03 means March; the year is 2000+ (0x2068>>9) = 2000 + 0x10 =2016; |
| Equilibrium | 2 Byte | Each bit represents the balance of each string, 0 means off, 1 means on, which means 1~16 strings |
| Equilibrium_High | 2 Byte | Each bit means each string is balanced, 0 means off, 1 means on, which means 17~32 strings, and supports up to 32 strings |
| Protection status | 2 Byte | Each bit represents a protection status, 0 is unprotected, 1 is protected. See note 1: |
| Keep | 1 Byte |  |
| remaining battery | 1 Byte | Indicates the percentage of remaining capacity |
| FET control status | 1 Byte | MOS indicates status, bit0 means charging, bit1 means discharging, 0 means MOS is off, 1 means on |
| Number of battery strings | 1 Byte | Number of battery strings |
| Number of NTC | 1 Byte | Number of NTC |
| N NTC content | 2*N Byte | The unit 0.1K adopts absolute temperature transmission, 2731+(actual temperature*10), 0 degrees = 2731 25 degrees = 2731+25*10 = 2981; |

Note 1: Description of protection status:

BIT 0 monomer overvoltage protection

BIT 1 monomer undervoltage protection

BIT 2 whole set of overvoltage protection

BIT 3 whole group undervoltage protection

BIT 4 charging over temperature protection

BIT 5 charging low temperature protection

BIT 6 discharge over temperature protection

BIT 7 discharge low temperature protection

BIT 8 charging overcurrent protection

BIT 9 discharge overcurrent protection

BIT 10 short circuit protection

BIT 11 front-end detection IC error

BIT 12 software locks MOS

BIT 13~ BIT 15 reserved

- Read battery cell voltage

Host sends: DD A5 04 00 FF FC 77

BMS response: DD 04 00 1E 0F 66 0F 63 0F 63 0F 64 0F 3E 0F 63 0F 37 0F 5B 0F 65 0F 3B 0F 63 0F 63 0F 3C 0F 66 0F 3D F9 F9 77

The data content structure of the response frame is as follows:

| Data content | length | the data shows |
| --- | --- | --- |
| First string cell voltage | 2Byte | Unit mV, high order first |
| Second string cell voltage | 2Byte | Unit mV, high order first |
| The third string cell voltage | 2Byte | Unit mV, high order first |
| Nth string cell voltage | 2Byte | Unit mV, high order first |

- Read the hardware and software version number of the protection board

Host sends: DD A5 05 00 FF FB 77

BMS response: DD 05 00 0A 30 31 32 33 34 35 36 37 38 39 FD E9 77

The data content structure of the response frame is as follows:

| Data length N | the data shows |
| --- | --- |
| BYTE N | The reply content is ASCII code (for example, the hardware version is H-XXXX) |

- Read the private data of the protection board user

Machine send: DD A5 06 00 FF FA 77

BMS response: DD 06 00 0A 30 31 32 33 34 35 36 37 38 39 FD E9 77

The data content structure of the response frame is as follows:

| Data length N | the data shows |
| --- | --- |
| BYTE N | The reply content is ASCII code (than "23562455") |

- Control MOS instruction

The host sends a control MOS command:
		Host sends: DD 5A E1 02 00 XX CH CL 77
		BMS response: DD E1 00 00 CH CL 77

The comparison table of XX and MOS actions is as follows:

| XX value | MOS action |
| --- | --- |
| 0x00 | Release the software to close the MOS tube action |
| 0x01 | Software closes charging MOS, and releases software closes discharging MOS |
| 0x02 | The software closes the discharge MOS, and the software closes the charging MOS. |
| 0x03 | Software turns off charge and discharge MOS at the same time |

Example: The host sends DD 5A E1 02 00 02 FF 1B 77 to indicate that the software closes the discharge MOS;